## Slide 1
FLOOD FREQUENCY ANALYSIS USING EXTREME VALUE DISTRIBUTION IN PENINSULAR MALAYSIA BASED ON L-MOMENT METHOD
NUR AMIRA BINTI ABDUL AZIZ (2023184923)
SUPERVISOR: DR. BASRI BIN BADYALINA

## Slide 2
AGENDA OVERVIEW
03
04
17
05
18
BACKGROUND OF STUDY
PROBLEM STATEMENT
CONCLUSION
METHOD OF ANALYSIS
06-10
RECOMMENDATION
METHODOLOGY
11-16
RESULT OF STUDY
19
REFERENCES

## Slide 3
  Malaysia experienced frequent floods, especially during the monsoon seasons (Southwest: May–Sept; Northeast: Nov–March).
  Heavy rainfall during monsoons affecting areas like Kelantan, Terengganu, and Johor.
  Floods led to community displacement, damaged infrastructure, and economic loss.
  Understanding flood patterns was essential.
  This study used 63 years of data and focus on three statistical models including Generalized Extreme Value (GEV), Generalized Pareto (GPA), and Generalized Logistic (GLO) distributions.
BACKGROUND OF STUDY
03

## Slide 4
  Flooding in Peninsular Malaysia was a significant hazard, endangering individuals, infrastructure, and ecosystems.
  The increased frequency and severity of floods underscored the urgent need for improved prediction and control strategies.
  Flood frequency Analysis (FFA) was a statistical technique used.
  L-moments provided a more reliable estimation of probability distributions for extreme events compared to conventional moments.
PROBLEM STATEMENT
04

## Slide 5
METHOD OF ANALYSIS
Method of Analysis
Ranking the Performance Measure
L-Moment
Quantile Estimate
Research objectives
To develop and evaluate a precise flood frequency model using extreme value distributions for predicting the occurrence and magnitude of floods in Peninsular Malaysia’s river systems.
To utilise L-Moments for the estimation of parameters of extreme value distributions used in modelling flood data.
To estimate the return periods of various flood magnitudes by analysing historical streamflow data and applying extreme value distributions.
05

## Slide 6
METHODOLOGY
06

## Slide 7
METHODOLOGY
  The probability weight moment (PWM) generates the L-moment, introduced by J.R. Hosking (1990).
  Four unbiased estimator components and the first four sample estimators of L-Moment, derived L-Moment ratios.
L-MOMENT
07

## Slide 8
METHODOLOGY
08
EXTREME VALUE DISTRIBUTION
  Hamed & Rao (2019) presented the probability and cumulative density function of the GEV, GPA and GLO distributions.
  Utilising three parameters ( , , and ) was possible to calculate the quantile estimate for each distribution based on the return period.
Quantile estimate each distribution:

## Slide 9
  Accuracy Performance Measurement: There were five accuracy performance measurement used: the Mean Absolute Percentage Error (MAPE), Mean Absolute Error (MAE), Root Mean Square Error (RMSE), Root Mean Square Percentage Error (RMSPE), Coefficient of Determination ( )
  L-Moment Ratio Diagram:
  Proposed by Hosking and Wallis (1997) to choose an appropriate distribution that represented the streamflow data.
  Each distribution ratio diagram created with L-kurtosis against L-skewness by substituting value of t3 in the t4 calculation.
  Goodness of Fit: The Anderson-Darling Test and Kolmogorov-Smirnov Test implied by Hamed & Rao (2019) to evaluate the degree of fit between the distribution and the real dataset.
METHODOLOGY
09
PERFORMANCE MEASUREMENT

## Slide 10
METHODOLOGY
10
  The ranking was the final stage of implementation in the study.
  The distribution with the greatest score (3) was considered the best fit, while the one with the lowest score (1) was considered the least appropriate.
MEASUREMENT RANKING

## Slide 11
L-moment components | L-moment components | L-moment components | L-moment components
4.3715 | 1.6051 | 0.2264 | 0.2398
RESULT OF STUDY
1. L-MOMENT
where, mean ( ), scale ( ), skewness ( ), and kurtosis ( )
  The value 0.43715 reflecting the average magnitude of the flood events.
  The scale indicates moderate variation in flood magnitudes.
  The skewness signifies a positive asymmetry in the data distribution.
  The kurtosis signifies light tails in the distribution.
11

## Slide 12
 |  | Parameters | 
Distribution |  |  | 
GEV | 2.4109 | 3.0840 | 0.0454
GPA | 6.0547 | 0.3498 | 0.5055
GLO | 1.5531 | 4.0027 | -0.1411
2. ESTIMATION PARAMETER
where scale parameter ( ), location parameter ( ), and shape parameter ( )
  GPA indicate greater variability, range of flood magnitude the widest.
  GLO indicate flood magnitude generally high.
  GPA suggested heavy tail.
12

## Slide 13
L-CV (t2) | L-Skewness (t3) | L-Kurtosis (t4)
0.3672 | 0.1411 | 0.1494
3. L-MOMENT RATIO DIAGRAM
13
  The candidate distribution for the best distribution is GEV distribution.

## Slide 14
Distribution | GEV | GPA | GLO
AD | 0.3979 | 0.000009524 | 0.3684
K-S | 0.4244 | 0.1567 | 0.5923
MAPE | 0.2276 | 0.1271 | 0.3048
MAE | 0.5369 | 0.5827 | 0.5396
RMSE | 0.8883 | 1.1586 | 0.7842
RMSPE | 65.0587 | 19.9394 | 99.9211
 | 0.9180 | 0.8589 | 0.9366
Abbreviation: Anderson Darling (AD), Kolmogorov-Smirnov (K-S) Test, Mean Absolute Percentage Error (MAPE), Mean Absolute Error (MAE), Root Mean Square Error (RMSE), Root Mean Square Percentage Error (RMSPE), Coefficient of Determination ( )
4. GOODNESS-OF-FIT AND ACCURACY PERFORMANCE MEASURE
14

## Slide 15
Distribution | GEV | GPA | GLO
AD | 3 | 1 | 2
K-S | 2 | 1 | 3
MAPE | 2 | 3 | 1
MAE | 3 | 1 | 2
RMSE | 2 | 1 | 3
RMSPE | 2 | 3 | 1
 | 2 | 1 | 3
Total Score | 16 | 11 | 15
Abbreviation: Anderson Darling (AD), Kolmogorov-Smirnov (K-S) Test, Mean Absolute Percentage Error (MAPE), Mean Absolute Error (MAE), Root Mean Square Error (RMSE), Root Mean Square Percentage Error (RMSPE), Coefficient of Determination ( )
5. MEASUREMENT RANKING
  The best distribution is GEV.
15

## Slide 16
Return Period (year) | Probabilities (p) | Estimated Flood Discharge m³/s | Estimated Flood Discharge m³/s | Estimated Flood Discharge m³/s
Return Period (year) | Probabilities (p) | GEV | GPA | GLO
10 | 0.90 | 8.2412 | 8.2280 | 8.3828
50 | 0.98 | 11.7045 | 12.1111 | 10.6525
100 | 0.99 | 13.0923 | 14.0749 | 11.1536
6. QUANTILE ESTIMATE
16

## Slide 17
CONCLUSION
  Highlighted the practical and academic implications of integrating detailed data analysis into flood mitigation and regional planning.
  Identified GEV distribution as the most reliable model for predicting flood magnitudes, outperforming other methods in accuracy and goodness-of-fit tests.
  Quantile estimates from GEV predict flood discharges for 10, 50, and 100 years at 8.24 m³/s, 11.70 m³/s, and 13.09 m³/s, respectively.
17

## Slide 18
RECOMMENDATION
18
  Policymakers and engineers should optimise the use of GEV in flood control structures.
  Government and policymakers can employs quantile estimate to mitigate flood impacts.
  Future researcher can implement in other regions to validate the used of GEV model.

## Slide 19
REFERENCES
19
Hamed, K., & Rao, A. R. (2019). Flood frequency analysis. CRC press.
Hosking, J. R. M., & Wallis, J. R. (1997). Regional frequency analysis.

## Slide 20
THANK YOU